This master should be used by designers working on Port of Portland construction projects and by designers working for PDX tenants (“Tenants”).  Usage notes highlight a few specific editing choices, however the entire section should be evaluated and edited to fit specific project needs.

# SECTION 026100 – REMOVAL AND DISPOSAL OF CONTAMINATED SOILS

## GENERAL

DESCRIPTION

This section describes excavation and disposal of soil contaminated with petroleum and other products.

If the Contractor encounters suspected contaminated soil in the work area beyond that mentioned in the contract documents, the Contractor shall immediately stop all work in the area of the suspected contamination and notify the Port.  The Port will characterize contaminated soil, obtain profile for disposal, and determine the location of disposal.

RELATED WORK SPECIFIED ELSEWHERE

Item P-152, Excavation and Embankment

Section 312000, Site Clearing and Earthwork

Section 312300, Trenching, Backfilling, and Compacting

SUBMITTALS

Submit copies of all receipts for processing contaminated soil at the disposal facility.

DISPOSAL DOCUMENTATION

The Port will prepare all documentation required for characterization and disposal of contaminated soil at the disposal facility.

DEFINITIONS

Contaminated Soil:  Soil that produces a fuel or chemical odor, produces an oil sheen on the surface of water, has staining, contains debris or other visible indicators, or soil designated by the Port as contaminated.

## PRODUCTS

PLASTIC SHEETING

Minimum 6 mil polyethylene sheeting.

## EXECUTION

GENERAL

The Port will provide field and laboratory evaluation of materials suspected of being contaminated.

Notify the Port 48 hours before excavating in an area of known or suspected contamination.

The Port will designate which materials are contaminated and which are suitable for use in the work.

The Port will determine the disposition of all materials.

The Contractor shall assist the Port in collecting soil samples from excavator buckets or by briefly stopping work to allow observations or samples to be collected.

EXCAVATION AND STOCKPILING

All contaminated excavated material is the property of the Port and will be handled per direction by the Port.

Excavation to remove material determined by the Port to be contaminated shall be performed as described in Section 312300, Trenching, Backfilling, and Compacting, and shall be made to the depth and extent as determined by the Port.  Where necessary, backfill excavations with appropriate material as directed by the Port.

Provide adequate containment of and protection from contaminated material, suited to the type of contamination.  Follow all federal, state, and local requirements in excavating, loading, transporting, and otherwise handling or working around contaminated material.  The Contractor shall be responsible for meeting all regulatory requirements.

Replace “Section 312000, Site Clearing and Earthwork” with “Item P-152, Excavation and Embankment,” if applicable.

Contaminated stockpiles shall meet the requirements of Section 312000, Site Clearing and Earthwork.

Place contaminated soil in a stockpile separate from clean materials.

Stockpile contaminated soil on pavement or on plastic sheeting.  The perimeter of the plastic sheeting shall be elevated to prevent overland stormwater flow from contacting the contaminated soil.  Pavement may substitute for the plastic sheeting if there is a method for preventing stormwater flow into the stockpile (i.e., a curb on the uphill side of the stockpile).

Cover contaminated soil stockpile with plastic sheeting when the stockpile is not actively involved in construction.  Secure the plastic covering to ensure it stays in place and that stormwater runoff from the cover does not pond on the cover or contact the contaminated soil.

As directed by the Port, contaminated stockpiles shall remain in place for a minimum of 48 hours to allow for complete chemical analysis.

DISPOSAL

The Port will characterize contaminated soil and obtain the profile for disposal.

Choose B or C after discussing with Environmental.

Contaminated soil will be disposed of by a third party, hired by the Port.  The Contractor shall provide full access to the contaminated material stockpile.  This may include third party excavation, handling, and transportation equipment.

Contaminated soil shall be disposed of by the Contractor at a location determined by the Port.  Follow all federal, state, and local requirements and regulations in excavating, loading, transporting, disposing of, and otherwise handling the contaminated soil.

If contaminated soil is disposed of by the Contractor above, choose 1 or 2 after discussing with Environmental. Otherwise delete.

Haul contaminated soil to __________.

Haul contaminated soil to the Hillsboro Landfill located in Hillsboro, Oregon.

Notify the Port 72 hours before the initial haul to the designated disposal facility.

Notify the Port 48 hours before each subsequent haul to the designated disposal facility.

END OF SECTION 026100